## Slide 1
Project Aegis
Critical Design Review
Team Members:
Yvonne Villapudua, Janet Blancas, Jimmy Lopez, Isabella Molina, and Lillian Chang

## Slide 2: Launch Vehicle

## Slide 3
Launch Vehicle Dimensions
Booster Section
Middle Section
Forward Section
Length: 119 in
Diameter: 6.08 in

## Slide 4: Launch Vehicle Materials
Main materials:
Blue Tube 2.0
Aircraft plywood

## Slide 5
Section | Estimated Mass (lbs)
Aft | 18.60
Middle | 6.95
Forward | 13.80
Mass Statement

## Slide 6
Launch Vehicle | Estimated Mass (lbs) | Estimated Mass with 25% Increase (lbs)
Launch vehicle (on launch pad) | 40.09 | 50.11
Launch vehicle (before landing) | 34.44 | 43.05
Total Mass of Launch Vehicle
Mass Margin: 24lbs

## Slide 7
CG
CP
Stability, Center of Gravity, and Center of Pressure
Stability Margin with Motor: 3.33
Stability Margin without motor: 5.37
CG
CG
CP
CP

## Slide 8: Key Design Features
Fiberglass laminated airframe and fins
Payload position
Parachute compartment position

## Slide 9: Motor Selection

## Slide 10: General Motor Information
The selected motor is an Aerotech L1420R
Diameter: 75 mm
Length: 17.44 in
Launch weight is 10.06 lbs.
Empty weight is 4.41 lbs.

## Slide 11: Motor Characteristics
Maximum thrust of 1662 N
Average thrust of 1424 N
Total impulse of 4616 Ns
Burn time 3.24 sec

## Slide 12: Thrust to Weight Ratio
The thrust to weight ratio is 7.97
The launch vehicle must have a thrust greater than the weight of the launch vehicle in order to take off

## Slide 13: Motor Thrust Curve of Aerotech L1420R

## Slide 14: Kinetic Energy of the Independent Sections
Section | Kinetic Energy with Drogue (ft.-lbf) | Kinetic Energy with Main Parachute (ft.-lbf)
Forward | 1350.75 | 36.92
Middle | 643.75 | 17.60
Aft | 1260.71 | 34.46

## Slide 15: Drift Values
Wind speed | Drift with Main Parachute
5 | 328.10
10 | 738.88
15 | 954.96
20 | 2111.76

## Slide 16: Recovery System

## Slide 17: Recovery Subsystem Components
Parachutes
Avionics Bay
Electrical Components
TeleGPS

## Slide 18: Electrical Components
Missile Work RRC2+ Altimeter
E-matches
Batteries
Key Switches
Bulk Plate and Attached Components

## Slide 19: Electronic Schematics

## Slide 20: Parachute and Harness
Parachute | 
Drogue | Main
24” Elliptical | 120”Toroidal
Recovery Harness |  | 
Harness Type | Harness Width | Harness Length
Tubular Nylon | 1” | Drogue: 45 ft Main: 35 ft

## Slide 21
Launch Vehicle Section | V (drogue) (ft/s) | V (main) (ft/s)
Forward | 78.02 | 15.62
Middle | 78.02 | 15.62
Aft | 78.02 | 15.62
Descent Rates

## Slide 22
Sub-Scale Design and Flight Analysis

## Slide 23: Sub-scale Launch Vehicle Summary
Diameter: 4.01 in
Stability(with motor): 2.85 caliber
Mass(without motor): 213.94 oz
Mass(with motor): 267.39 oz
Motor: Aerotech K550W
Thrust to weight ratio: 5.34

## Slide 24: Tests of the Staged Recovery System
Parachute packing and running test
Altimeter test
Sub-scale ground ejection test

## Slide 25: Sub-scale Ground Ejection Test
Trial | Drogue black powder mass (g) | Main black powder mass (g) | Body Tube Separated | Parachute Released | Parachute Damage | Other Damage
1 | 1.67 | 0.81 | No | No | No | No
2 | 2.67 | 1.81 | Yes | Yes | No | Yes
Ejection canister

## Slide 26: Sub-scale Recovery System
Parachute | Harness | Altimeter
30” Drogue | 30’ | Missile Works RRC2+ Altimeters
72” Main | 30’ | 

## Slide 27: Sub-scale Test Launch
Launch Day Conditions | 
Conditions | Values
Temperature (°F) | 35.6
Time of Launch | 1:35pm
Wind Speed and Direction | 3 mph headed east
Humidity | 21.04
Cloud Coverage | Clear sky
Precipitation | None
Pressure (psi) | 14.76
December 18, 2016 Lucerne Dry Lake

## Slide 28: Sub-scale Flight Results
Stable flight
Successful recovery
Apogee | 
Estimated | Reported
4063.49 ft | 4237 ft
Range | 
Estimated | Reported
1496.97 ft | 2112 ft

## Slide 29: Fragile Material Protection Payload

## Slide 30
Final Payload Dimensions
Complete Container
Lid & Adapter
Outer Shell

## Slide 31: Final Payload Dimensions Cont.
Inner Chamber
Radiation Shield
Aerogel

## Slide 32: Final Design Overview
Lid
Adapter
Inner Rack
Inner Chamber
Aerogel
Radiation Shield
Outer Shell

## Slide 33: Mass Statement and Mass Margin
Payload total calculated weight: 8.5 lbs
Mass margin for payload: 1 lb

## Slide 34: Key Design Features

## Slide 35: Key Design Features Cont.

## Slide 36: Interfaces

## Slide 37: Internal and External Interfaces
Recovery system interface
Motor mount interface
Payload interface
Ignition interface
Launch rail interface

## Slide 38: Payload Integration
Insertion
Extraction
Stability
Security

## Slide 39: Status of Requirements Verification

## Slide 40: Status of launch Vehicle Requirements Verification
Reusable rocket and motor
Recording official altitude
Launch success
Vehicle prohibitions

## Slide 41: Status of Recovery System Requirements Verification
Ground ejection test
Kinetic energy and descent velocity calculations
Deployment
Electronics

## Slide 42: Status of Payload Requirements Verification
Multiple objects
Unknown object

## Slide 43: Status of Safety Requirements Verification
Launch and safety checklist
Safety officer
Rules and regulation

## Slide 44: Status of General Requirements Verification
Outreach
Team derived requirements

## Slide 45
Test Plans and Procedures

## Slide 46: Subscale Tests and Procedures
Sub-scale payload
  Impact test
  Heat resistance test
Parachute test
Altimeters
Ground ejection test
Center of gravity

## Slide 47: Full-scale Test Plans and Procedures
Payload
  Impact test
  Heat resistance test
  Compartment adjustment test
  Weight test
Parachute
Ground ejection
Test launch
GPS testing