## Slide 1
Project Aegis
Preliminary Design Review
Team Members:
Yvonne Villapudua, Janet Blancas, Jimmy Lopez, Isabella Molina, and Lillian Chang

## Slide 2: Launch Vehicle

## Slide 3
Launch Dimensions
Dimensions:
Length: 119.00”
Diameter: 6.08”
Notes: Rebecca

## Slide 4: Launch Vehicle Materials
Main materials:
Blue Tube 2.0
Aircraft Plywood

## Slide 5
CG
CP
CG
CP
Stability, Center of Gravity, and Center of Pressure
Stability Margin with Motor: 2.47
Stability Margin without motor: 4.60

## Slide 6: Motor Selection

## Slide 7: General Motor Information
The selected motor is an Aerotech L1170-FJ
Diameter: 75mm
Length: 26.18”
Launch weight is 9.68lbs
Empty weight is 3.51lbs

## Slide 8: Motor Characteristics
Burn time 3.71s
Maximum thrust of 1489N
Average thrust of 1136.9N
Total impulse of 4222.6Ns

## Slide 9: Motor Thrust Curve of Aerotech L1170-FJ

## Slide 10: Thrust to Weight Ratio
The thrust to weight ratio is 7.5
The launch vehicle must have a thrust greater than the weight of the launch vehicle in order to take off

## Slide 11: Launch Vehicle Subsystems

## Slide 12: Propulsion Subsystem
Motor
Motor retainer
Motor mount

## Slide 13
Structural and Aerodynamic Stability Subsystem
Fins
Nose Cone
Airframe

## Slide 14: Recovery Subsystem Components
Parachutes
Avionics Bay
Electrical Components
TeleGPS
Avionics Bay
Main Parachute Compartment
Payload Bay
Drogue Parachute Compartment

## Slide 15: Avionics Bay
Bulk Plates
U-bolt
Ejection Canisters
Hole for wires
Terminal Block

## Slide 16: Electrical Components
Missile Work RRC2+ Altimeter
E-matches
Batteries
Key Switches
Bulk Plate and Attached Components

## Slide 17: Electronic Schematics

## Slide 18: TeleGPS
TeleGPS/Ground Station
  TeleDongle
  3-Element Yagi Antenna
  434.55 MHz
  10 mW

## Slide 19: Fragile Material Protection Payload

## Slide 20
Primary Payload Design

## Slide 21
Individual Components
Container lid
Inner Chamber Rack
Inner Chamber
Outer Shell
Radiation shield

## Slide 22
Inner Rack

## Slide 23: Requirement Compliance Plan

## Slide 24
Launch Vehicle
Requirement Compliance Plan
Reusable rocket
Recording official altitude
Launch success
Vehicle Prohibition
Notes: Logan

## Slide 25: Recovery System Requirement Compliance Plan
Ground ejection test
Deployment
Electronics

## Slide 26: Fragile Material Protection Requirement Compliance Plan
Multiple Objects
Unknown object

## Slide 27: Safety Requirement Compliance Plan
Launch and Safety checklist
Safety Officer
Rules and Regulation