## Slide 1
Project Aegis
Flight Readiness Review
Team Members:
Yvonne Villapudua, Janet Blancas, Jimmy Lopez, Isabella Molina, and Lillian Chang

## Slide 2: Launch Vehicle

## Slide 3
Launch Vehicle Dimensions
Booster Section
Middle Section
Forward Section
Length: 119 in
Diameter: 6.08 in

## Slide 4: Key Design Features
Fiberglass laminated airframe and fins
Payload position
Parachute compartment position

## Slide 5
Section | Measured Mass (lbs.)
Aft | 14.40
Middle | 8.92
Forward | 12.23
Mass Statement

## Slide 6
Launch Vehicle | Actual Mass (lbs.) | Estimated Mass (lbs.)
Launch vehicle (on launch pad) | 45.61 | 39.35
Launch vehicle (before landing) | 39.96 | 33.70
Total Mass of Launch Vehicle
Mass Margin: 18.28 lbs

## Slide 7: Motor

## Slide 8: General Motor Information
The selected motor is an Aerotech L1420R
Diameter: 75 mm
Length: 17.44 in
Launch weight is 10.06 lbs.
Empty weight is 4.41 lbs.

## Slide 9: Motor Characteristics
Maximum thrust of 1662 N
Average thrust of 1424 N
Total impulse of 4616 Ns
Burn time 3.24 sec

## Slide 10: Static Margin Diagram
Stability Margin (with motor): 3.33
Stability Margin (without motor): 5.37

## Slide 11: Launch Vehicle Performance

## Slide 12: Thrust to Weight Ratio
The thrust to weight ratio is 7.97
The launch vehicle must have a thrust greater than the weight of the launch vehicle in order to take off
Rail exit velocity – 77.29 fps

## Slide 13: Kinetic Energy of the Independent Sections
Section | Kinetic Energy at Take Off (ft-lbf) | Kinetic Energy at Apogee (ft-lbf) | Kinetic Energy at Landing (ft-lbf)
Forward | 1320.09 | 1350.75 | 36.92
Middle | 628.32 | 643.75 | 17.60
Aft | 1232.09 | 1260.71 | 34.46

## Slide 14: Predicted Altitude of the Launch Vehicle at Different Wind Speeds
Wind speed (mph) | Predicted Altitude (ft)
5 | 5287.63
10 | 5249.87
15 | 5186.92
20 | 5097.90

## Slide 15: Predicted Drift Values at Different Wind Speeds
Wind speed | Predicted Drift (ft)
5 | 328.10
10 | 738.88
15 | 954.96
20 | 2111.76

## Slide 16: Full-scale Flight Test

## Slide 17: Full-scale Test Launch
Launch Day Conditions | 
Conditions | Values
Elevation | 2530 ft
Time of Launch | 1:00 pm
Wind Speed | 10. 01 mph
Temperature | 61°F
Precipitation | 0%
Pressure (psi) | 14.72
February 4, 2017 Friends of Amateur Rocketry

## Slide 18: Recovery System

## Slide 19
Launch Vehicle Section | V (drogue) (ft/s) | V (main) (ft/s)
Forward | 78.18 | 12.92
Middle | 78.18 | 12.92
Aft | 78.18 | 12.92
Descent Rates

## Slide 20: Full-scale Recovery System
Parachute | 
Drogue | Main
24” Elliptical | 120”Toroidal
Recovery Harness |  | 
Harness Type | Harness Width | Harness Length
Tubular Nylon | 1” | Drogue: 45 ft Main: 35 ft

## Slide 21: Tests of the Staged Recovery System
Parachute packing and running test
Drop test
Sub-scale ground ejection test
GPS test

## Slide 22: Parachute Packing and Running Test

## Slide 23: Full-scale Ground Ejection Test
Trial | Drogue black powder mass (g) | Main black powder mass (g) | Body Tube Separated | Parachute Released | Parachute Damage | Other Damage
1 | 2.36 | 4.87 | No | No | No | No
2 | 2.86 | 5.37 | Yes | Yes | No | No

## Slide 24: Drop Test
Notes: Sheer pin early deployment

## Slide 25: GPS Test

## Slide 26: Test Plans and Procedures

## Slide 27: Full-scale Test Plans and Procedures
Payload
  Impact test
  Heat resistance test
  Compartment adjustment test
  Weight test
Recovery Subsystem
  Parachute test
  Ground ejection test
  Drop test
  Test launch
  GPS testing

## Slide 28: Fragile Material Protection Payload

## Slide 29
Payload Dimensions
Complete Container
Lid & Adapter
Outer Shell

## Slide 30: Payload Dimensions Cont.
Inner Chamber
Radiation Shield
Aerogel

## Slide 31: Payload Design Overview
Lid
Adapter
Inner Rack
Inner Chamber
Aerogel
Radiation Shield
Outer Shell
Sealing Disk

## Slide 32: Payload Design Overview

## Slide 33: Key Design Features

## Slide 34: Key Design Features Cont.

## Slide 35: Payload Integration
Insertion
Extraction
Stability
Security

## Slide 36: Interfaces

## Slide 37: Interfaces with Ground System
Interfaces with GPS
Interfaces with rail system
Interfaces with ignition system

## Slide 38: Summary of Requirements Verification

## Slide 39: Summary of Launch Vehicle Requirements Verification
Reusable rocket and motor
Recording official altitude
Launch success
Vehicle prohibitions

## Slide 40: Summary of Payload Requirements Verification
Multiple objects
Unknown object